## Slide 1
Blackout 2.4
Unveiling 2.4 GHz Network Vulnerabilities

## Slide 2
Team Behind Blackout 2.4
Our team, guided by the expertise of Sir Inzamam has meticulously developed and executed this project to shed light on prevalent wireless security concerns.
Hassan Iftikhar
UW-23-CY-BS-002
Ibrar-ul-Hassan
UW-23-CY-BS-018
UW-23-CY-BS-013
Azfar Waqas

## Slide 3
Why Blackout 2.4? Unpacking Our Motivation
The omnipresence of 2.4 GHz wireless networks in our daily lives, coupled with a general lack of security awareness in common devices, forms the core motivation for this project. We aim to expose how readily these networks can be compromised.
Heavy Reliance on 2.4 GHz Wireless Networks
From home Wi-Fi to everyday IoT gadgets, the 2.4 GHz band is the backbone of our connected world, making its security paramount.
Weak Security Awareness in Common Devices
Many consumer-grade devices come with default or easily exploitable security settings, presenting significant vulnerabilities.
Need to Understand Real-World Wireless Attacks
Our project seeks to demystify complex wireless attacks, demonstrating their practical execution and impact to foster better defense strategies.

## Slide 4
The Crowded & Vulnerable 2.4 GHz Spectrum
The 2.4 GHz spectrum is a double-edged sword: universally adopted yet inherently vulnerable. Its crowded nature makes it susceptible to interference and various forms of attack that are often difficult to detect.
Crowded and Vulnerable Spectrum
Numerous devices compete for bandwidth, leading to congestion and making it easier for malicious signals to blend in.
Attacks are Easy to Perform but Hard to Detect
The simplicity of launching many wireless attacks belies the complexity of identifying them, leaving networks exposed.
Limited Visibility of Spectrum Misuse
Without specialized tools, users and administrators often remain unaware of illicit activities happening within their wireless environment.
The Crowded & Vulnerable
2.4 GHz Spectrum

## Slide 5
Our Objectives: Illuminating Wireless Threats
PROJECT BLACKOUT 2.4
NETWORK SECURITY
"Blackout 2.4" is a network security project focused on the detailed analysis and exploitation of the 2.4 GHz wireless spectrum. Our core objectives center around bringing clarity to the often-invisible threats lurking in our wireless environments.
1
Analyze 2.4 GHz Wireless Activity
We aim to meticulously monitor and dissect traffic within this band to identify anomalies and potential vulnerabilities.
2
Demonstrate Common Wireless Attacks
Through practical demonstrations, we will showcase how readily prevalent attacks can be executed.
3
Highlight Security Risks and Misuse Scenarios
Our findings will underscore the real-world implications of insecure wireless practices and potential malicious uses.

## Slide 6
Targeted Frequencies: The 2.4 GHz ISM Band
Our project specifically focuses on the 2.4 GHz Industrial, Scientific, and Medical (ISM) band, a global unlicensed frequency spectrum crucial for a myriad of wireless communications.
2.4 GHz ISM Band
The primary target for our analysis, due to its widespread adoption and inherent vulnerabilities.
Wi-Fi (802.11 b/g/n)
The most common technology in this band, connecting countless devices to the internet.
Bluetooth & BLE Devices
Short-range communication protocols for peripherals, audio, and IoT, also operating within this frequency.
DE-Authentication Frames

## Slide 7
Attack Vector Showcase: Demonstrating Wireless Exploits
This project will practically demonstrate a range of common wireless attacks, showcasing their mechanisms and potential impact on unsuspecting users and networks.
1
Wi-Fi Deauthentication
Forcing devices off a Wi-Fi network, disrupting connectivity and creating opportunities for further attacks.
2
Evil Portal
Setting up a rogue access point to intercept credentials or deliver malicious content.
3
Rick Roll Attack
A humorous yet disruptive attack redirecting users to unexpected content.
4
Clone & Spam Attacks
Duplicating network identities and flooding targets with overwhelming traffic.
5
Bluetooth Spamming
Overwhelming Bluetooth devices with unwanted connection requests and notifications.

## Slide 8
System Overview
To effectively execute and monitor these demonstrations, we developed a portable embedded attack platform. This self-contained system allows for versatile and on-the-go wireless exploitation and analysis.
Portable Embedded Attack Platform
Designed for mobility, enabling security testing in various environments.
Touch-Based Interface
Intuitive control and real-time feedback for seamless interaction during demonstrations.
Wireless Attack Execution & Monitoring
Capable of launching various attacks while simultaneously observing their effects.

## Slide 9
Hardware Backbone: The Foundation of Blackout 2.4
The physical components forming the core of our attack platform are carefully selected for their capabilities in wireless communication and interactive display.
ESP32 Microcontroller
The brain of our system, providing powerful processing and integrated Wi-Fi/Bluetooth capabilities.
2.8” TFT Touch Display
Enables user interaction and visual feedback, making the platform user-friendly and intuitive.
Breadboard & Jumper Wires
Facilitates rapid prototyping and flexible connections between components for testing and development.

## Slide 10
Software Core: Powering the Exploitations
The intelligence of our Blackout 2.4 platform stems from its robust software components, specifically tailored for wireless interaction and user control.
01
ESP32 Firmware
Custom-developed software loaded onto the microcontroller, orchestrating all hardware functions.
02
Wi-Fi & BLE Libraries
Essential programming interfaces enabling seamless communication and manipulation of the 2.4 GHz spectrum.
03
Touch UI & Control Logic
The interactive element, translating touch inputs into commands and presenting real-time data to the user.

## Slide 11
Blackout 2.4: Core Functional Capabilities
Blackout 2.4 is designed with a suite of functional capabilities that allow for comprehensive analysis and simulation of wireless network vulnerabilities. These features provide a powerful toolkit for understanding and demonstrating potential attack vectors in a controlled environment.
Spectrum Scanning
The device can actively scan and identify all available Wi-Fi networks in its vicinity, mapping out the wireless landscape. This allows for detailed reconnaissance of target environments.
Channel Monitoring
Beyond simple scanning, Blackout 2.4 provides real-time monitoring of specific Wi-Fi channels, observing data traffic and identifying active devices and potential points of interest.
Attack Triggering
Equipped with the ability to initiate various simulated attacks, the system can demonstrate the impact of different exploit techniques, providing practical insights into network security.
Real-Time Feedback
During simulations, Blackout 2.4 offers immediate feedback on the success and impact of triggered actions, allowing for instantaneous adjustments and deeper understanding of attack dynamics.

## Slide 12
Understanding the Deauthentication Attack
The deauthentication attack is a fundamental and highly effective method for disrupting wireless network connectivity. This simulation demonstrates a critical vulnerability within the 802.11 standard.
Mechanism of Attack
Forces clients off Wi-Fi networks by sending spoofed deauthentication frames.
Exploits the lack of authentication in 802.11 management frames.
No encryption or authentication is required for these frames, making them highly susceptible to abuse.
This type of attack essentially tells a client device that it is no longer authorized to be connected to a specific Wi-Fi network, causing it to disconnect. While seemingly simple, its implications for network stability and user access are significant.
A deauthentication attack highlights a core design flaw in legacy Wi-Fi protocols, making it a critical demonstration for understanding denial-of-service vulnerabilities.

## Slide 13
Simulating an Evil Portal Attack
The Evil Portal attack showcases a sophisticated form of social engineering by creating a deceptive environment to trick users into divulging sensitive information. This demonstration highlights the dangers of trusting unknown network access points.
Fake Access Point Creation
Blackout 2.4 can simulate an unauthorized Wi-Fi access point, often mimicking legitimate networks. This 'evil twin' lures unsuspecting users into connecting to it instead of the real network.
Credential Harvesting
Once connected, users are often redirected to a fake login page (the "portal") that closely resembles a legitimate service (e.g., public Wi-Fi login, email, social media). This simulates the process of capturing usernames and passwords.
Social Engineering in Action
This attack is a prime example of social engineering, where human psychology is exploited to gain access to information. It underscores the importance of verifying network legitimacy before entering credentials.
NOVELTY

## Slide 14
Exploring Bluetooth Attack Vectors
Beyond Wi-Fi, Blackout 2.4 also explores vulnerabilities within Bluetooth Low Energy (BLE) protocols, demonstrating how seemingly innocuous features can be exploited for disruptive purposes. These attacks highlight the need for robust security across all wireless communication standards.
BLE Advertisement Spam
The device can flood an area with numerous fake BLE advertisements, overwhelming nearby devices and making it difficult for legitimate connections to be established or maintained.
Device Confusion & Disruption
By creating a multitude of phantom devices, real devices can become confused, leading to connection failures, battery drain, and general operational instability for Bluetooth-enabled gadgets.
Misuse Risks Illustrated
This demonstrates how common Bluetooth features, intended for convenience, can be repurposed for malicious activities, underscoring the broader security challenges in IoT and connected devices.

## Slide 15
Testing and Verifying Attack Execution
Rigorous testing was conducted to ensure the Blackout 2.4 system reliably performs the simulated attacks. The results consistently demonstrated successful execution, stable performance, and immediate, observable effects on target networks and devices.
100%
Attack Success Rate
All simulated attacks, including deauthentication, evil portal, and Bluetooth spam, executed with a 100% success rate in controlled test environments.
ESP32
Stable Performance
The ESP32 microcontroller maintained stable operation throughout all testing phases, handling resource-intensive tasks without crashes or significant performance degradation.
Real-Time
Immediate Response
Target devices and networks exhibited instantaneous responses to the triggered attacks, confirming the effectiveness and real-time impact of the Blackout 2.4 system.
Observational data confirmed that client devices were successfully disconnected, fake access points were established, and Bluetooth devices were overwhelmed with advertisements, validating the system's capabilities.

## Slide 16
Ethical Considerations and Responsible Usage
The development and use of tools like Blackout 2.4 come with significant ethical responsibilities. It is paramount that such technologies are used strictly for educational purposes and within controlled, authorized environments to prevent harm and ensure compliance with legal and ethical guidelines.
Educational Use Only
Blackout 2.4 is designed as a learning tool to help students and professionals understand wireless security vulnerabilities and defense mechanisms. It is not intended for malicious activities.
Lab-Controlled Environment
All demonstrations and testing were conducted within isolated, lab-controlled settings where no external networks or unauthorized devices were affected. This ensures responsible research and development.
No Real User Data Targeted
During any simulated credential harvesting or disruption, no actual user data was targeted, collected, or compromised. The focus remains purely on demonstrating the attack mechanism, not on exploiting individuals.
Users are strictly advised to adhere to all local laws and regulations regarding wireless network testing and ethical hacking. Misuse of such tools can lead to severe legal consequences.

## Slide 17
Conclusion: The Pervasive Vulnerabilities of 2.4 GHz
Our exploration with Blackout 2.4 conclusively demonstrates that the widely used 2.4 GHz wireless spectrum, despite its ubiquity, remains highly susceptible to various straightforward yet highly effective attacks. This highlights an urgent need for increased awareness and more robust security practices.
2.4 GHz is Highly Exploitable
The common 2.4 GHz band, used by Wi-Fi and Bluetooth, is prone to vulnerabilities stemming from outdated protocols and widespread device compatibility requirements. This makes it a prime target for various forms of attack.
Attacks Are Simple Yet Effective
As demonstrated, attacks like deauthentication and evil portals require minimal technical sophistication to execute but can have significant disruptive impacts, affecting connectivity and data security.
Security Awareness is Critical
The ease with which these attacks can be performed underscores the critical importance of user and administrator awareness. Education, strong password practices, and vigilance against suspicious network behavior are essential defense mechanisms.

## Slide 18
Thank You for Your Attention!
Any Questions?
.